## Slide 1: Elastic Scheduling for Harmonic Task Systems
Marion Sudvarg, Ao Li, Daisy Wang,
Sanjoy Baruah, Jeremy Buhler, Chris Gill, Ning Zhang,
Pontus Ekberg (Uppsala University)
Thursday, May 16
RTAS 2024

## Slide 3: Real-Time Systems
Increasingly execute in dynamic environments

## Slide 4
Image courtesy wired.co.uk
Notes: Lidar pipeline: must recognize car, but must also do so on time to avoid collision

## Slide 5: Real-time systems must adapt to maintain temporal guarantees even on overloaded computational platforms
Elastic Scheduling
Giorgio Buttazzo, Giuseppe Lipari, and Luca Abeni. “Elastic task model for adaptive rate control.” RTSS 1998

## Slide 6
Notes: Task utilizations are traditionally decreased by increasing their periods

## Slide 7
Elastic Scheduling of Implicit-Deadline Tasks with Harmonic Periods

## Slide 8
Image courtesy https://projects.asl.ethz.ch/datasets/doku.php?id=kmavvisualinertialdatasets
Simultaneous localization and mapping (SLAM) systems

## Slide 9
Harmonic Periods
SLAM systems synchronize frames from multiple input sources
Visual
Inertial
Lidar
ORB-SLAM3
𝛕1, T=2
𝛕0, T=1
𝛕2, T=4

## Slide 10: This Talk
Selecting harmonic periods
Elastic scheduling with harmonic periods
Case study: atmospheric aerosol sampling
Case study: ORB-SLAM3
Open questions in computational complexity

## Slide 11
The Harmonic
Period Problem
Mitra Nasri, Gerhard Fohler, Mehdi Kargahli. “A Framework to Construct Customized Harmonic Periods for Real-Time Systems.” ECRTS 2014.

## Slide 12
The Harmonic Period Problem
T1
T2
T3
x2
x3
x2
x3
x2

## Slide 13
Non-Overlapping Intervals
T1
T2
T3
s1
e1
s2
e2
e3
s3

## Slide 14
Non-Overlapping Intervals
T1
T2
T3
s1
e1
s2
e2
e3
s3

## Slide 15
s1
s2
e2
e3
s3
s4
e4
e5
s5
s6
e6
e7
s7
s8
e8
e9

## Slide 16
s1
s2
e2
e3
s3
s4
e4
e5
s5
s6
e6
e7
s7
s8
e8
e9
≤
s1
s1
e2
e3
e2
e3
e4
e5
e4
e5
e6
e7
e6
e7
e9
e9

## Slide 17
s1
e9

## Slide 18
s1
en
= k
Upper bound on Projected Harmonic Zones
k2

## Slide 19
Overlapping Intervals
T1
T2
T3
x2
x2
x1

## Slide 20
The Harmonic
Elastic Problem

## Slide 21
Problem
Proportional compression may not maintain the harmonic period relationships

## Slide 22
Solution
Use equivalent constrained optimization

## Slide 23
Thidapat (Tam) Chantem, Xiaobo (Sharon) Hu, and Michael D. Lemmon. “Generalized Elastic Scheduling.” RTSS 2006

## Slide 24
Problem
Solving this constrained-optimization problem is NP-hard

## Slide 25
Ordered Harmonic Elastic Problem
ORB-SLAM3
𝛕1, T=2
𝛕0, T=1
𝛕2, T=4

## Slide 26
Build a lookup table offline
to enable fast online compression in response to changes in available utilization

## Slide 27
1. Enumerate “Projected Harmonic Intervals”
T1
T2
T3
x1
x1

## Slide 28
1. Enumerate “Projected Harmonic Intervals”
T1
T2
T3
x2
x1

## Slide 29
2. Build lookup table matching ranges of utilization to optimal PHI
For n tasks, table size at most
x1, x1, x7
x3, x2, x1
x2, x4, x3
x3, x1, x2
x1, x2, x1
x1, x3, x2

## Slide 30
For n tasks, table size at most
1000 sets each,

## Slide 31
3. Adjust online to changes in available utilization
For n tasks, table size at most
Binary search over table
Polynomial!

## Slide 32
For n tasks, table size at most
1000 sets each,

## Slide 33
Case Studies

## Slide 34: The Fast Integrated Mobility Spectrometer (FIMS)
Notes: The Fast Integrated Mobility Spectrometer (FIMS) is a flown instrument that characterizes atmospheric aerosols. Recent efforts to enable real-time measurements of aerosol particle sizes (e.g., to instruct the aircraft to follow an aerosol plume) achieved the desired performance on a Raspberry Pi 4.The improved computational pipeline illustrated captures and processes images to detect particles, grouping them into fixed-duration windows of particle inlet time. Using matrix inversion, it converts instrument responses from particle spatial coordinates to determine the particle size distribution within each window. “Housekeeping” (HK) data readouts from other sensors (e.g., temperature and pressure) are synchronized with the inversion process, and are used to determine if a new data inversion matrix must be computed. Harmonic execution guarantees a fixed, integral number of time windows associated with each job. This stabilizes the fraction of particles lost during the inversion process, ensuring a consistent representation of particle distribution and maintaining measurement accuracy, while also bounding the latency between a particle’s inlet time and its subsequent inclusion in the reported size distribution.

## Slide 35: The Fast Integrated Mobility Spectrometer (FIMS)
Image courtesy https://www.seilergeodrones.com/shop/dji-matrice-300-rtk/

## Slide 36: The Fast Integrated Mobility Spectrometer (FIMS)
HK Data
Process
Image
Particle Time Window Queue
HK Data Queue
Data
Inversion

## Slide 37
Selecting elastic constants to minimize result error within the constraints of schedulability

## Slide 38
HK Data
Data Inversion
Process Image
Error

## Slide 39
With utilization limited to 0.1-0.5 by a high-priority interfering task,
no FIMS tasks missed their deadlines

## Slide 40: ORB-SLAM3
Camera
Images
IMU
Tracking
Mapping

## Slide 41
Camera
Mapping
IMU
Error Relative Translational Error

## Slide 42: ORB-SLAM3

## Slide 43: Key Takeaways
Pseudo-polynomial algorithm for harmonic period selection problem
Building LUT offline enables polynomial-time elastic adaption in response to changes in utilization bound
Effective when applied to applications with dataflow pipelines: FIMS and ORB-SLAM3

## Slide 44
NP
P
Harmonic Period Problem
Harmonic Elastic Problem
Ordered Harmonic Elastic Problem

## Slide 45
Strongly NP
Weakly NP
Integer Factor
P
Harmonic Period Problem
Harmonic Elastic Problem
Ordered Harmonic Elastic Problem

## Slide 46
Strongly NP
Weakly NP
Integer Factor
P
Harmonic Period Problem
Harmonic Elastic Problem
Ordered Harmonic Elastic Problem

## Slide 47
Strongly NP
Weakly NP
Integer Factor
P
Harmonic Period Problem
Harmonic Elastic Problem
Ordered Harmonic Elastic Problem

## Slide 48
Strongly NP
Weakly NP
Integer Factor
P
Harmonic Period Problem
Harmonic Elastic Problem
Ordered Harmonic Elastic Problem
?

## Slide 49
Strongly NP
Weakly NP
Integer Factor
P
Harmonic Period Problem
Harmonic Elastic Problem
Ordered Harmonic Elastic Problem
?

## Slide 50
Strongly NP
Weakly NP
Integer Factor
P
Harmonic Period Problem
Harmonic Elastic Problem
Ordered Harmonic Elastic Problem
?
?

## Slide 51
Strongly NP
Weakly NP
Integer Factor
P
Harmonic Period Problem
Harmonic Elastic Problem
Ordered Harmonic Elastic Problem
?
?