## Slide 1: Improved Implicit-Deadline Elastic Scheduling
SIES 2024
Chengdu, China
Marion Sudvarg, Chris Gill, Sanjoy Baruah
msudvarg@wustl.edu www.sudvarg.com
This work was supported by NSF grants CPS-2229290
and CNS-2141256 and a WashU seed grant

## Slide 2: Real-Time Systems
Increasingly execute in dynamic environments

## Slide 3
Image courtesy wired.co.uk
Notes: An example of this is in the quickly-developing domain of self-driving cars, where perception pipelines must process data from multiple sensors, such as the pictured LIDAR stream, in a timely fashion. The computational workloads and latency requirements depend on external factors; a crowded city street presents a more challenging environment than a highway in the countryside.

## Slide 4: Elastic Scheduling
Real-time systems must adapt to maintain temporal guarantees even on overloaded computational platforms
Giorgio Buttazzo, Giuseppe Lipari, and Luca Abeni. “Elastic Task Model for Adaptive Rate Control.” RTSS 1998

## Slide 5
Elastic scheduling allows tasks to reduce («compress») their utilizations
Elastic Scheduling
Maximum desired utilization, nominal execution in uncompressed state | Minimum utilization necessary to maintain correct or safe execution | Elasticity, representing relative adaptability
Maximum desired utilization, nominal execution in uncompressed state | Minimum utilization necessary to maintain correct or safe execution | Elasticity, representing relative adaptability
Each task’s utilization is decreased from its maximum proportionally to its elasticity until the system becomes schedulable
Task utilizations constrained to remain above the minimum

## Slide 6: How is utilization compressed?
Extend Task Periods
Control Systems
Buttazzo et al. “Quality-of-Control Management in Overloaded Real-Time Systems.” IEEE Transactions on Computers 2007
Reduce Task Workloads
Gamma-Ray Burst Localization
Sudvarg, Buhler, Chamberlain, Gill, Buckley, Chen. “Parameterized Workload Adaptation for Fork-Join Tasks with Dynamic Workloads and Deadlines.” RTCSA 2023.
Image Masking
Sudvarg, Wang, Buhler, Gill. “Subtask-Level Elastic Scheduling.” RTSS 2024.
Atmospheric Aerosol Monitoring
Simultaneous Localization and Mapping (SLAM)
Sudvarg, Li, Wang, Baruah, Buhler, Gill, Zhang, Ekberg. “Elastic Scheduling for Harmonic Task Systems.” RTAS 2024.

## Slide 7: When is utilization compressed?
Offline schedulability analysis
Dynamic workloads due to external environment
Online changes in available resources
Admission of new tasks
Task overruns in mixed-criticality systems
Zhuoran Sun, Marion Sudvarg, Chris Gill. “Elastic Scheduling for Graceful Degradation of Mixed-Criticality Systems.” RTNS 2024.

## Slide 8: Algorithms that assign task utilizations under the elastic scheduling model must be efficient during online adaptation

## Slide 9: Our Contributions
Efficient algorithms for implicit-deadline elastic scheduling
Linear-time online adaptation for utilization bound schedulability analysis
(Uniprocessor Scheduling, Fluid Scheduling, Partitioned EDF)
Binary search for more complex analysis
(Heuristic Partitioned EDF)
Quadratic-time online adaptation for Global EDF

## Slide 10: Uniprocessor Scheduling

## Slide 11: Original Algorithm
Recall: task utilizations decreased proportionally to elasticity until schedulable
Giorgio Buttazzo, Giuseppe Lipari, and Luca Abeni. “Elastic Task Model for Adaptive Rate Control.” RTSS 1998

## Slide 12: Faster Algorithm
Sort!
Compress in a single traversal
“Amount” of compression to reach minimum utilization

## Slide 13: Task Admission Times on Raspberry Pi 3B+
Median
Max

## Slide 14: Fluid Scheduling

## Slide 15: Fluid Scheduling
Convenient abstraction for multicore scheduling
Every task is assigned a fraction of a processor at each instant in time
Schedulable on cores so long as:
Total utilization does not exceed
Individual task utilizations do not exceed 1

## Slide 16
Initialize and Sort
Compress

## Slide 17: Partitioned EDF

## Slide 18: Partitioned EDF
Fluid scheduling is easy to analyze but impractical to implement
Partitioned EDF is more straightforward to implement
Find a partition of tasks onto cores where total utilization on each core does not exceed 1
This is bin packing – strongly NP-complete!

## Slide 19: Let’s revisit the original elastic model
Recall: task utilizations decreased proportionally to elasticity until schedulable
Amount of compression
Goal: find the smallest that guarantees schedulability

## Slide 20: Original Algorithm
James Orr, Sanjoy Baruah. “Multiprocessor Scheduling of Elastic Tasks.” RTNS 2019.
Linear search for the smallest λ with precision ε in
For each λ, use pseudo-polynomial bin packing heuristics to check schedulability

## Slide 21: Improvement 1: Use Binary Search

## Slide 22: Improvement 2: Use Utilization Bound
First-fit and best-fit decreasing bin packing guarantee a utilization bound of
Sanjoy Baruah. “Partitioned EDF Scheduling: A Closer Look.” Real-Time Systems, 2013.

## Slide 23: Improvement 2: Use Utilization Bound

## Slide 24: Improvement 2: Use Utilization Bound

## Slide 25: Global EDF

## Slide 26: Global EDF
On cores, the active jobs with earliest deadlines execute
Schedulable on cores so long as:

## Slide 27: Global EDF

## Slide 28: Global EDF: Algorithm
Utilization-bound compression!
Problem: We do not know which task will have after compression
Solution: Try all tasks!
Initial sort only needs to be done only once.

## Slide 29: Conclusions
Elastic scheduling adapts task utilizations in the face of overload.
Online adaptation must be fast.
We have presented fast elastic scheduling algorithms for implicit-deadline tasks:
  Uniprocessor scheduling
  Fluid scheduling
  Partitioned EDF
  Global EDF

## Slide 30: Future Work
Can we extend these techniques to other scheduling algorithms?
Hyperbolic bound for RM
Partitioned RM
Global RM
Algorithm PriD

## Slide 31: Thank You!
www.sudvarg.com
msudvarg@wustl.edu